## Slide 1: Island County Shoreline Hard Armor Mapping & Change Analysis
Teams Presentation | May 7, 2024
Notes: Introductions (Andrea & Lauren)

## Slide 2: Puget Sound Interconnected components
Notes: Andrea

## Slide 3: SHORELINE ARMOR
Impacts of Shore Armor
  Burial of beach
  Loss of backshore berm
  Increase wave reflection
  Beach scour/erosion
  Loss of fines (sands)
  Impacts to littoral drift
  Reduced sediment input
  Proliferation and expansion
  Habitats simplified/lost
Notes: Andrea

## Slide 4: Mapping SHORELINE ARMOR in Island County
Mapping Objectives
  Repeat Methods from 2016 mapping
  Measure Armor Change
    Characterize nature of change
  Pair with Permit Analysis
    Evaluate types of permits and actions
Notes: Andrea

## Slide 5: Shoreline Armor Mapping Methods
Boat-based mapping
Desktop post-processing and analysis
Association of armor changes with permit records
Notes: Lauren

## Slide 6: Shoreline Armor mapping methods
Boat-based mapping
  GNSS GPS + Laser Rangefinder
  Digital Field Form
  High-tide cycle for shallow areas
Notes: Lauren
GPS unit with real-time kinematic corrections in the field paired with a laser rangefinder to do offset mapping
Will explain in a little more detail
Map by boat in order to move nimbly and get access to shores
Use digital field form for efficiency and consistency
Scheduled mapping to reach shallow areas at high tides

## Slide 7: Laser Offset Mapping
How it works:
  Collect a GPS point
  Within digital field form, “offset” the GPS point
  Fire the laser rangefinder at the mapping target
  The GPS point is shifted in FieldMaps to the target location
Notes: Lauren

## Slide 8: Post-Processing and Analysis Approach
Desktop post-processing and analysis
  Compared “pre-snap” and ShoreZone-conforming armor geometry
  Analyzed for changes in:
    Presence/absence
    Elevation
    Condition
  Summarized by shoretype, forage fish impacts
Notes: Lauren

## Slide 9: Permit Analysis approach
Unify and summarize permit records across jurisdictions
Associate tax parcels with permit records by Parcel ID
Extend coastal parcels to intersect armor records (ShoreZone Shoreline-conforming)
Spatially intersect and summarize mapped change (armor line) against issued permits (from tax parcels)
Parcel Number | Jurisdiction | Permit Number | Permit Type | Permit Description | Project Name | Project Description | Permit Issued | Permit Status Description | Armor Permit | Soft shore permit | Other permit (dock footing, etc.) | After the fact | Emergency | Approved | Install | Repair | Remove | Replace | Modify
R13202-268-4820 | Oak Harbor |  | Shoreline maintenance exemption | Armor repair and stormwater outfall repair | Armor repair and stormwater outfall repair | Armor repair and stormwater outfall repair 80 LF | 10/19/2018 | Approved | 1 |  |  |  |  | 1 |  | 1 |  |  | 
R13232-173-0200 | Island County | 373/20 | PL-SHE-II | Shoreline Exemption, Type II | Demolish existing house, replace bulkhead and construct new SFR and appurtenances |  |  | Approved with Conditions | 1 |  |  |  |  | 1 |  |  |  | 1 | 
R13233-410-3750 | Coupeville | SSD-23-001 |  | Sea wall | Sea wall | Sea wall |  | Denied | 1 |  |  |  |  |  | 1 |  |  |  | 
R13332-238-0170 | Island County | 273/22 | PL-SHE-II | Shoreline Exemption, Type II | Hayes bulkhead | Replacement of rock bulkhead with concrete bulkhead |  | Permit application is technically complete | 1 |  |  |  |  |  |  |  |  | 1 | 
R13332-247-0220 | Island County | 159/19 | PL-SHE-II | Shoreline Exemption, Type II | Repair of existing 120 linear ft rock riprap bulkhead | Repair of existing 120 linear ft rock riprap bulkhead | 6/14/2019 | Approved with Conditions | 1 |  |  |  |  | 1 |  | 1 |  |  | 
Notes: Lauren

## Slide 10: Shoreline Armor Mapping & Change
Notes: Lauren

## Slide 11: Shoreline Armor Change REsults
Island County armor change (2016 to 2023):
  391 new armor segments
  Mappers observed active shore armor construction at 4 locations
  64% of new armor installed adjacent to existing armor
Notes: Lauren
391 new armor segments identified between 2016 and 2023 mapping events
Of those, 117 segments were greater than 20 feet in length
Of 4 armor sites noted in construction during mapping, One was confirmed to be unpermitted
By length, 64% of new armor

## Slide 12: Shoreline Armor CHANGE Results
Accretion shoreforms and feeder bluff most frequently armored
  59% of new armor on accretion shoreforms
  20% of new armor on feeder bluffs
Notes: Lauren
Armoring of accretion shoreforms – loss of beach resilience to SLR
Armoring of bluffs – loss of sediment inputs to sustain down-drift beaches and forage fish spawning habitat

## Slide 13: Shoreline Armor CHANGE Results
30% of forage fish spawning habitat was armored in 2023
  29% of habitat armored in both 2016 and 2023
  New armor on 1.3% of habitat
  Armor removed from 1% of forage fish spawning habitat
Notes: Lauren
165,100 feet of ffs habitat armored in 2023 mapping

## Slide 14: Permit Analysis
New Armor + Permit Associations (Count of Parcels)
Notes: Lauren
New armor associated with 325 parcels
Of those parcels,
15 (4%) had an approved permit for new armor
2 (1%) had submitted a permit for new armor, but were denied
308 (95%) submitted no permit applications

## Slide 15: Permit Analysis
New Armor + Permit Associations
(Length)
New Armor + Permit Associations
(Count of Parcels)
Notes: Lauren
14,119 feet of new armor across 325 parcels
New armor was permitted along 1,930 feet (14% of new armor)
New armor was installed with a denied permit along 150 feet (2% of new armor by length)
New armor installed with no permit records along remaining 12,040 feet (84%)

## Slide 16: Permit Analysis
Widespread permitted and unpermitted change
  Most change clustered in existing developments
  Some parcels had more than one permit
Example sites:
Notes: Lauren
Example – Utsalady Bay
Black line – existing armor
White line – new armor
Red parcels – new armor mapped, no issued permit
Orange parcels – armor modification mapped, no issued permit
Example – Admiralty Bay
Black line – existing armor
White line – new armor
Red hatched parcel – new armor with permit

## Slide 17: Discussion
Considerable lengths of unpermitted and permitted armor change were documented since 2016
Additional verification of armor on unpermitted activities should be conducted before pursuing action:
  Mapping event photos and historical air photos
  Legacy permits
Ongoing compliance monitoring and armor change mapping are valuable tools for enforcement and preserving long-term shoreline functions
Notes: Andrea

## Slide 18: Question & Answer
Notes: Andrea